## Slide 1: Data and Computer Communications
Chapter 1
Introduction

## Slide 2: A Communications Model
Source
generates data to be transmitted
Transmitter
Converts data into transmittable signals
Transmission System
Carries data
Receiver
Converts received signal into data
Destination
Takes incoming data

## Slide 3: Simplified Communications Model - Diagram

## Slide 4: Key Communications Tasks
Transmission System Utilization
Interfacing
Signal Generation
Synchronization
Exchange Management
Error detection and correction
Addressing and routing
Recovery
Message formatting
Security
Network Management

## Slide 5: Simplified Data Communications Model

## Slide 6: Networking
Point to point communication not usually practical
Devices are too far apart
Large set of devices would need impractical number of connections
Solution is a communications network

## Slide 7: Simplified Network Model

## Slide 8: Wide Area Networks
Large geographical area
Crossing public rights of way
Rely in part on common carrier circuits
Alternative technologies
Circuit switching
Packet switching
Frame relay
Asynchronous Transfer Mode (ATM)

## Slide 9: Circuit Switching
Dedicated communications path established for the duration of the conversation
e.g. telephone network

## Slide 10: Packet Switching
Data sent out of sequence
Small chunks (packets) of data at a time
Packets passed from node to node between source and destination
Used for terminal to computer and computer to computer communications

## Slide 11: Frame Relay
Packet switching systems have large overheads to compensate for errors
Modern systems are more reliable
Errors can be caught in end system

## Slide 13: Asynchronous Transfer Mode
ATM
Evolution of frame relay
Little overhead for error control
Fixed packet (called cell) length
Anything from 10Mbps to 1Gbps
Constant data rate using packet switching technique

## Slide 14: Local Area Networks
Smaller scope
Building or small campus
Usually owned by same organization as attached devices
Data rates much higher
Usually broadcast systems
Now some switched systems and ATM are being introduced

## Slide 15: Protocols
Used for communications between entities in a system
Must speak the same language
Entities
  User applications
  e-mail facilities
  terminals
Systems
  Computer
  Terminal
  Remote sensor

## Slide 16: Key Elements of a Protocol
Syntax
  Data formats
  Signal levels
Semantics
  Control information
  Error handling
Timing
  Speed matching
  Sequencing

## Slide 17: Protocol Architecture
Task of communication broken up into modules
For example file transfer could use three modules
File transfer application
Communication service unit
Network access unit

## Slide 18: Simplified File Transfer Architecture

## Slide 19: A Three Layer Model
Network Access Layer
Transport Layer
Application Layer

## Slide 20: Network Access Layer
Exchange of data between the computer and the network
Sending computer provides address of destination
May invoke levels of service
Dependent on type of network used (LAN, packet switched etc.)

## Slide 21: Transport Layer
Reliable data exchange
Independent of network being used
Independent of application

## Slide 22: Application Layer
Support for different user applications
e.g. e-mail, file transfer