## Slide 1: PHYSICAL LAYER

## Slide 2: PHYSICAL LAYER – PURPOSE
The OSI Physical layer transport the bits that makes up a Data Link layer frame
across the network media
This layer accepts a complete frame from the Data Link layer and encodes it as a series of signals that are transmitted onto the local media.

## Slide 3
The delivery of frames across the local media requires the following Physical layer elements:
The physical media and associated connectors
A representation of bits on the media
Encoding of data and control information
Transmitter and receiver circuit on the network devices
At this stage of the communication process, the user data has been segmented by the Transport layer, placed into packets by the Network layer, and further encapsulated as a frames by the Data Link layer.
The purpose of the Physical layer is to create the electrical, optical, or microwave signal that represents the bits in each frame.
These signals are then sent on the media one at a time.
It is also the job of the Physical layer to retrieve these individual signals from the media and restore them to their bit representations

## Slide 4: Physical Layer – Operation The media carries signals, one at a time, to represent the bits that make up the frame.
There are three basic forms of network media on which data is represented:
Copper cable
Fiber
Wireless
The representation of the bits - that is, the type of signal - depends on the type of
media.
For copper cable media, the signals are patterns of electrical pulses.
For fiber, the signals are patterns of light.
For wireless media, the signals are patterns of radio transmissions.

## Slide 6: Physical Layer - Standards
The protocols and operations of the upper OSI layers are performed by software and are designed by software engineers
The services and protocols in the TCP/IP suite are defined by the Internet Engineering Task Force (IETF). Similar to technologies associated with the Data Link layer, the Physical layer technologies are defined by organizations such as:
The International Organization for Standardization (ISO)
The Institute of Electrical and Electronics Engineers (IEEE)
The American National Standards Institute (ANSI)
The International Telecommunication Union (ITU)
The Electronics Industry Alliance/Telecommunications Industry Association (EIA/TIA)
National telecommunications authorities such as the Federal Communication Commission (FCC) in the USA.

## Slide 8: Physical Layer Technologies and Hardware
Four areas of the Physical layer standards:
Physical and electrical properties of the media
Mechanical properties of the connectors
Bit representation by the signals (encoding)
Definition of control information signals
Hardware components such as network adapters (NICs), interfaces and connectors, cable materials, and cable designs are all specified in standards associated with the Physical layer.

## Slide 9: Physical layer Fundamental Principles
The three fundamental functions of the Physical layer are:
The physical components
Data encoding
Signalling

## Slide 10
The physical component
Electronic hardware devices, media and connectors that transmit and carry the signals to represent the bits.
Encoding
method of converting a stream of data bits into a predefined code.
Codes : groupings of bits used to provide a predictable pattern that can be recognized by both the sender and the receiver.
Predictable patterns : distinguish data bits from control bits and provide better
media error detection.
Signalling
The method of representing the bits.
The Physical layer standards must define what type of signal represents a "1" and "0". This can be as simple as a change in the level of an electrical signal or optical pulse or a more complex signalling method.

## Slide 11: PHYSICAL SIGNALLING AND ENCODING: REPRESENTING BITS

## Slide 12: DATA CARRYING CAPACITY
Can be measured in three ways:
Bandwidth
-the capacity of a medium to carry data in a given amount of time.
Throughput
-the actual transfer rate of data over the medium in a period of time.
Goodput
-the transfer rate of actual usable data bits.

## Slide 13: PHYSICAL MEDIA- CONNECTING COMMUNICATION

## Slide 14: COPPER MEDIA
Copper media has standards defined for each of the following :
Type of copper cabling used
Bandwidth of the communication
Type of connectors used
Pinout and color codes of connections to the media
Maximum distance of the media

## Slide 15
conducts electrical signals very well, but it has its limitations
data travels on copper cables as small pulses of electrical voltage cause it easily distorted by outside noise and signal attenuation
cable type with shielding or twisting of the pairs of wires are designed to minimize signal degradation

## Slide 16: UNSHIELDED TWISTED PAIR(UTP) CABLE
used in Ethernet LANs
eight wires twisted into four color-coded pairs and then wound inside a cable jacket
colored pairs identify the wires for proper connection at the
terminals

## Slide 17
each wire in the pair carries current in the opposite direction, keeping them close together with twisting will cause the magnetic fields on the wire pair to cancel each other
magnetic interference from wires within the cable is called
crosstalk
rate of twisting in each pair of wires is different so that each pair self cancels and reduces crosstalk to a minimum
UTP Cabling Standards :
cable types
cable lengths
connectors
Cable termination
method of testing cable

## Slide 18: CATEGORIES OF UTP CABLE
Each category indicates a level of bandwidth performance as defined by the IEEE
Cat3
Cat5-UTP cable improvements allowed 100-megabit transmissions
Cat5e-enabled full-duplex Fast Ethernet gigabit transmission over
UTP cable
Cat6-allow higher performance and less crosstalk
most common UTP cable connector in LAN devices is an RJ-45
connector
RJ-45 jack is larger and has a different cable termination

## Slide 19
required order of the wires in the connector, called the pinout, varies according to where the cable fits in the network
Each device connection requires a specific cable pinout to ensure that signals transmitted on a wire at one end arrive on the correct “receive” circuit at the other end of the cable.

## Slide 21: OTHER COPPER CABLE TYPES
Coaxial Cable
has a single, coated copper wire center
outer metal mesh that acts as both a grounding circuit
an electromagnetic shield to reduce interference
Outer layer is the plastic cable jacket

## Slide 22
for transporting high radio frequency signal over wire
HFC combines the electrical properties of coax and the bandwidth and distance benefits of fiber-optic cable
Shielded twisted-pair (STP) cable
twisting the pairs of wire inside the cable to reduce noise
shielding the cable in a wire mesh
more expensive than other available cable

## Slide 23: COPPER MEDIA SAFETY
Separate data and electrical power cabling
Connect cables correctly
Inspect cabling installations for damage
Ground equipment correctly

## Slide 24: FIBER MEDIA
Fiber-optic cable is very different from copper, yet both effectively carry data over networks.
Copper uses electrical voltage to represent data on the wire, fiber-optic cable uses light pulses conducted through special glass conductors to carry data.
The fiber-optic cable is engineered to be as pure as possible and to allow reliable light signals to traverse the medium.
The standards and performance levels of fiber are constantly improving.

## Slide 25: Challenges when installing fiber in a network.
Higher cost of fiber-optic cable and connectors
Special training required for installing fiber
Fiber cable also requires more special handling than copper cable.(fragile)
Advantages of fiber media
It is immune to the earth ground and lightning concerns
Low noise immunity
Low signal loss
High bandwidth
Long distances

## Slide 27
Basic types of
fiber-optic cable:
single-mode
multimode cables.

## Slide 28: WIRELESS MEDIA
Carry electromagnetic radio signals that represent the binary data of the data-link frame.
Transmit and receive signals through the medium of the open atmosphere.
Advantages :
  Cost savings on wiring
  Convenience of host mobility
Disadvantages :
  Susceptible to interference
  Security risk

## Slide 29
The IEEE and telecommunications industry standards for wireless data communications cover both the data link and physical layers. Following are four common data communications standards that apply to wireless media:
Standard IEEE 802.11: Commonly referred to as Wi-Fi,
802.11 is a wireless LAN (WLAN) technology that uses a contention or nondeterministic system with a carrier sense multiple access/collision avoid (CSMA/CA) media access process.
Standard IEEE 802.15: Wireless Personal-Area Network (WPAN): Commonly known as Bluetooth, 802.15 uses a device- pairing process to communicate over distances from 1 to 100 meters.

## Slide 30
Standard IEEE 802.16: Commonly known as WiMAX (Worldwide Interoperability for Microwave Access), 802.16 uses a point-to-multipoint topology to provide wireless broadband access.
Global System for Mobile Communication (GSM) : Includes physical layer specifications that enable the implementation of the Layer 2 General Packet Radio Service (GPRS) protocol to provide data transfer over mobile cellular telephony networks.

## Slide 31: WIRELESS LAN
A common wireless data implementation is enabling devices to wirelessly connect through a LAN. In general, a wireless LAN requires the following network devices:
Wireless access point (AP): Concentrates the wireless signals from users and connects, usually through a copper cable, to the existing copper-based network infrastructure such as Ethernet
Wireless NIC adapter: Provides wireless communication capability to each network Host As the technology has developed, a number of WLAN Ethernet-based standards have emerged. Care needs to be taken in purchasing wireless devices to ensure compatibility and interoperability.

## Slide 33: Coaxial
BNC
F TYPE (male)
F TYPE (female)

## Slide 34
N TYPE (male)
N TYPE (female)

## Slide 35: Unshielded twisted pair (UTP)
RJ45 plug

## Slide 36: FIBER MEDIA CONNECTORS

## Slide 37
LC
connector

## Slide 38
Fiber-optic cabling is much more specialized than copper cable, and installing or repairing fiber requires special training and equipment. Three common fiber repair problems are as follows:
Misalignment
End gaps where fibers do not completely touch
Poorly finished ends causing poor clarity
When terminating fiber-optic cable, it is important to have the ends properly aligned, fused, and polished so that signaling remains strong and dispersion is at a minimum.